## Slide 1: Chapter 2
Computer Hardware – Storage Systems

## Slide 2: Storage Systems
Storage holds data, instructions, and information for future use
Consists of two parts
Storage Device
Storage Media

## Slide 3: Storage Systems
Storage is nonvolatile where as RAM memory is volatile
Two operations associated with storage
Reading - Process of transferring items from storage media to memory
Writing - Process of transferring items from memory to storage media

## Slide 4: Storage Capacity
Capacity refers to the number of bytes (characters) a storage media can hold.
Kilobyte (KB)
1 thousand
Megabyte (MB)
1 million
Gigabyte (GB)
1 billion
Terabyte (TB)
1 trillion
Petabyte (PB)
1 quadrillion
Exabyte (EB)
1 quintillion
Zettabyte (ZB)
1 sextillion
Yottabyte (YB)
1 septillion

## Slide 5: Hard Drives
Magnetic hard drives contain one or more round pieces of metal (called hard disks or platters) that are coated with a magnetizable substance.

## Slide 6: Hard Drives - Parts
Mounting Shaft
Read/Write head
Hard Disks
Access Mechanisms

## Slide 7: Hard Drives – Three Types
Internal
External
Removable

## Slide 8: Hard Drives – Organization
Tracks – data is stored on circular tracks
Sectors– pie shaped groups of sectors
Clusters– one or more sectors form clusters, the smallest storage area on a disk.
Track 13 –Disk 1 top
Track 13 –Disk 1 bottom
Track 13 –Disk 2 top
Track 13 –Disk 2 bottom
Track 13 –Disk 3 top
Track 13 –Disk 3 bottom
Track 13 –Disk 4 top
Track 13 –Disk 4 bottom
Cylinder – a vertical stack of tracks

## Slide 9: Hard Drives – Access Time
The total time that it takes for a hard drive to read or write data is called the disk access time and requires the following:
  Seek time - The read/write heads move to the cylinder that contains (or will contain) the desired data.
  Rotational delay - The hard disks rotate into the proper position so that the read/write heads are located over the part of the cylinder to be used.
  Data movement time - Reading the data from the hard disk to memory, or transfers from memory and is stored on the hard disk.

## Slide 10: Hard Drives – Disk Cache
A disk cache holds data that has recently been read from the hard drive.
If that data is needed soon in memory it is retrieve from the cache rather then from the hard drive when they are requested.

## Slide 11: Hard Drives - SSD
Solid state drives use the same type of memory used in USB drives.
Much faster in accessing information over the standard hard drive
More stable then hard drives

## Slide 12: Optical Discs
Flat, round, portable metal discs made of metal, plastic, and lacquer

## Slide 13: Optical Discs

## Slide 14: Data Storage on a CD/DVD
single track spirals to edge of disc
disc sectors

## Slide 15: Parts of a Optical Discs Player
disc label

## Slide 16: Parts of a Optical Discs Player
laser diode
disc label

## Slide 17: Parts of a Optical Discs Player
laser diode
prism
disc label

## Slide 18: Parts of a Optical Discs Player
laser diode
prism
lens
disc label

## Slide 19: Parts of a Optical Discs Player
laser diode
prism
light- sensing diode
lens
disc label

## Slide 20: Parts of a Optical Discs Player
laser diode
prism
light- sensing diode
lens
pit
disc label

## Slide 21: Parts of a Optical Discs Player
laser diode
prism
light- sensing diode
lens
pit
land
disc label

## Slide 22: Reading Data
laser diode
prism
light- sensing diode
lens
pit
land
disc label
Step 1. Laser diode shines a light beam toward disc

## Slide 23: Reading Data
laser diode
prism
light- sensing diode
lens
pit
land
disc label
Step 2. The light passes through the prism and is focused by lens on to the metal layer of the disc.

## Slide 24: Reading Data
laser diode
prism
light- sensing diode
lens
pit
land
disc label
Step 3. If light strikes a land, it is reflected off the prism into the light sensing diode.
This represents a 1 in binary
1

## Slide 25: Reading Data
laser diode
prism
light- sensing diode
lens
pit
land
disc label
Step 4. If light strikes a pit, it is scattered and no light reaches the light sensing diode
This represents a 0 in binary
1
0

## Slide 26: Flash Memory
Flash memory is a chip-based storage medium that represents data using electrons.

## Slide 27: Flash Memory – Memory Cards
One of the most common types of flash memory media is the flash memory card—
a small card containing
  flash memory chips
  controller chip
  other electrical components
  metal contacts

## Slide 28: Flash Memory - USB
USB flash drives consist of flash memory media integrated into a self-contained unit that contains;
  flash memory chips
  controller chip
  other electrical components
  metal contacts
connects to a computer or other device via a standard USB port and is powered via the USB port.

## Slide 29: Network Storage and Online/Cloud Storage Systems
Remote storage - A storage device that is accessed through a local network or through the Internet.
Cloud storage - Remote storage accessed via the Internet

## Slide 30: Smart Cards
A smart card is a credit card–sized piece of plastic that contains computer circuitry containing
  a processor
  memory
  storage.
Used in secure access system.