## Slide 1: Chapter 4 Computer Networks – Part 1
Networks, network characteristics, data transmission

## Slide 2: Learning Objectives
Explain what networks are
Identify network characteristics
Understand how data is transmitted over a network

## Slide 3: Common uses for computer networks
Sharing an Internet connection among several users
Sharing application software, printers, and other resources
Facilitating Voice over IP (VoIP), email, videoconferencing, IM, and other communications applications
Working collaboratively
Exchanging files among network users and over the Internet
Connecting the computers and entertainment devices located within a home

## Slide 4: Networking Applications:
Internet
Telephone
Television and Radio Broadcasting
GPS
Monitoring Systems
Multimedia Networking
Collaborative Computing
Telecommuting
Videoconferencing
Telemedicine

## Slide 5: Network Characteristics
Topics Covered:
  Wired vs. Wireless Networks
  Network Topologies
  Network Architectures
  Network Size and Coverage Area

## Slide 6: Wired vs. Wireless Networks
Wired network -computers and other devices on the network are physically connected via cabling to the network.
Wireless network - wireless signals are used to send data through the air between devices, instead of using physical cables.
Hotspots - wireless networks found in public locations.
Many networks are accessible by both wired and wireless technologies.

## Slide 7: Connecting to Wi-Fi

## Slide 8: Network Topologies
The physical topology of a computer network indicates how the devices in the network are arranged.
The three most common physical topologies are:

## Slide 9: Network Topologies
Star network - A network in which all the net-worked devices connect to a central device through which all network transmissions are sent.
Bus network - A network that uses a central cable to which all network devices connect.
Mesh network - A network that uses a number of different connections between network devices so that data can take any of several possible paths from source to destination.

## Slide 10: Network Architectures
Network Architectures: the way computers are designed to communicate
The two main types are:

## Slide 11: Network Architectures
Client- server networks include
  clients, which are computers and other devices on the network that request and use network resources
  servers, which are computers that are dedicated to processing cli-ent requests.

## Slide 12: Network Architectures
A peer- to- peer ( P2P) network
  has no central server.
  all the computers on the network work at the same functional level
  users have direct access to the computers and other devices attached to the network.

## Slide 13: Network Size and Coverage Area
A personal area network (PAN) is a network of personal devices that is designed to enable those devices to communicate and share data.

## Slide 14: Network Size and Coverage Area
A local area network (LAN) is a network that covers a relatively small geographical area, such as a home, an office building, or a school.

## Slide 15: Network Size and Coverage Area
A metropolitan area network (MAN) is a network designed to service a metropolitan area, typically a city or county.

## Slide 16: Network Size and Coverage Area
A wide area network (WAN) is a network that covers a large geographical area.
Best example the Internet

## Slide 17: Network Size and Coverage Area
An intranet is
  a private network, such as a company LAN, that is designed to be used by an organization’s employees
  is set up like the Internet with data posted on Web pages that are accessed with a Web browser
  A company network that is accessible to authorized outsiders is called an extranet.

## Slide 18: Network Size and Coverage Area
A virtual private network (VPN) is
a private, secure path across a public network (usually the Internet)
It is set up to allow authorized users private, secure access to the company network.

## Slide 19: Data Transmission
Topics Covered:
  Bandwidth
  Analog vs. Digital Signals
  Transmission Type and Timing
  Delivery Method

## Slide 20: Bandwidth
Bandwidth (also called throughput) is `the amount of data that can be transferred in a given time period.
Usualy measured in
  bits per second (bps)
  Kbps – thousands of bits per second
  Mbps - millions of bits per second
  Gbps – billions of bits per second.

## Slide 21: Analog vs. Digital Signals
Most networking media send data using digital signals, in which data is represented by only two discrete states: 0s and 1s.
Analog signals represent data with continuous waves.

## Slide 22: Transmission Type and Timing
With serial transmission, data is sent one bit at a time, one after the other along a single path.
When parallel transmission is used, the message is sent at least one byte at a time, with each bit in the byte taking a separate path.

## Slide 23: Transmission Type and Timing
When data is sent using serial transmission, one of the following three techniques is used to organize the bits being transferred so the data can be reconstructed after it is received:

## Slide 24: Transmission Type and Timing
Synchronous transmission - serial data transmission in which data is organized into groups or blocks of data that are transferred at regular, specifi ed intervals.:

## Slide 25: Transmission Type and Timing
Asynchronous transmission - serial data transmission in which data is sent when it is ready to be sent without being synchronized.

## Slide 26: Transmission Type and Timing
Isochronous transmission - serial data transmission in which data is sent at the same time as other related data.

## Slide 27: Transmission Type and Timing
Another distinction between the different types of transmissions is the direction in which transmitted data can move.
  Simplex transmission A type of data transmission in which data travels in a single direction only.
  Half- duplex transmission A type of data transmission in which data can travel in either direction, but only in one direction at a time.
  Full- duplex transmission A type of data transmission in which data can move in both directions at the same time.

## Slide 28: Delivery Method
Circuit switching –uses a dedicated path form the sender to the receiver.
Packet switching - messages are separated into small units called packets.
Broadcasting - when data is sent out, typically in packets, to all nodes on a network and is retrieved only by the intended recipient.