## Slide 1: MCTS Guide to Microsoft Windows 7
Chapter 8
Networking

## Slide 2: Objectives
Understand Windows 7 network components
Understand Windows 7 network architecture
Describe and configure Internet Protocol version 4
Describe and configure Internet Protocol version 6
Perform and monitor file sharing
Connect Windows 7 to the Internet
Describe and configure wireless networking
Configure Windows Firewall
Describe network bridging
Describe ad hoc and homegroup networks

## Slide 3: Networking Overview
Basic components of Windows 7 that support networking
  Network and Sharing Center
  Networks
  Connections

## Slide 4: Network and Sharing Center
Network and Sharing Center
  Central point in Windows 7 for managing the configuration of the network you are connected to
Areas
  Network map
  Active Network details
  Change your networking settings

## Slide 5: Network and Sharing Center Window

## Slide 6: Networks
Network location awareness
  Allows you to configure the security settings for each location type differently
Configuration settings for each location type are saved
Network Management
  View and manage all of the network locations your computer has connected to

## Slide 7: Networks Location Types

## Slide 8: Networks (cont'd.)
Network Discovery
  Provides you with an easy way to control how your computer views other computers on the network
    Advertises its presence on the network
  Options
    Turn on network discovery
    Turn off network discovery

## Slide 9: Connections
For each network device installed in your computer
  Connection is created to manage that network device
Clients and services
  Applications that use the network to communicate
  Client allows you to connect to a particular service running on a remote computer
  Service allows your computer to accept connections from and provide resources to a remote computer

## Slide 10: Area Connection Properties Dialog Box

## Slide 11: Connections (cont'd.)
Local Area Connection Properties
  Clients and services included with Windows 7
    Client for Microsoft Networks
    File and Printer Sharing for Microsoft Networks
    QoS Packet Scheduler
  Both the Client for Microsoft Networks and File and Printer Sharing for Microsoft Networks
    Use Server Message Block (SMB) version 2.0 protocol

## Slide 12: Connections (cont'd.)
Protocols
  Rules for communicating across the network
  Define how much data can be sent and the format of the data as it crosses the network
  Protocols supported by Windows 7
    Internet Protocol Version 4 (TCP/IPv4)
    Internet Protocol Version 6 (TCP/IPv6)
    Link-Layer Topology Discovery Mapper I/O Driver
    Link-Layer Topology Discovery Responder
Network driver
  Responsible for enabling communication between Windows 7 and a network device in your computer

## Slide 13: Network Architecture
Windows 7 includes several interfaces
  Make it easier for developers to create clients, services, protocols, and network drivers
Interfaces for networking in Windows 7
  Windows Sockets (Winsock) user mode
  Transport Device Interface (TDI)
  Winsock Kernel (WSK)
  Network Driver Interface Specification (NDIS)

## Slide 14: IP Version 4
Important configuration concepts of IPv4
  IP addresses
  Subnet masks
  Default gateways
  DNS
  WINS
  Methods for configuring IP
  Troubleshooting IPv4

## Slide 15: IP Addresses
Each computer must have a unique IP address to communicate on the network
IP addresses are most commonly displayed in dotted decimal notation
Several ranges of IP addresses are reserved for internal network use
  A proxy server or network address translation (NAT) must be used
    Provides Internet access to computers using these addresses

## Slide 16: IP Addresses (cont'd.)
IP Address Range | Network ( in CIDR notation)
192.168.0.0– 192.168.255.255 | 192.168.0.0/ 16
172.16.0.0– 172.31.255.255 | 172.16.0.0/ 12
10.0.0.0– 10.255.255.255 | 10.0.0.0/ 8
Addresses for internal networks

## Slide 17: Subnet Masks
IP address is composed of a network ID and a host ID
Subnet mask
  Defines which part of an IP address is the network ID and which part of the IP address is the host ID

## Slide 18: Default Gateways
Routers
  Control movement of packets through networks
Default gateway
  A router on the local network that is used to deliver packets to a remote network

## Slide 19: DNS
Domain Name System (DNS)
  Essential to communicate on a TCP/IP network
  Resolves host names to IP addresses
DNS is essential for Internet connectivity because most people use domain names, not IP addresses
  Accesses Internet servers such as Web sites

## Slide 20: WINS
Windows Internet Naming Service (WINS)
  Used to resolve NetBIOS names to IP addresses
  Stores information about services such as domain controllers
WINS is primarily used for backward compatibility with older NetBIOS based networks

## Slide 21: Methods for Configuring IP
To configure IP, you can use:
  Static configuration
  Dynamic configuration
  APIPA
  Alternate IP configuration
  Scripts
Dynamic Host Configuration Protocol (DHCP)
  An automated mechanism used to assign:
    IP addresses, subnet masks, default gateways, DNS servers, WINS servers, and other IP configuration information to network devices

## Slide 22: Methods for Configuring IP (cont'd.)

## Slide 23: Methods for Configuring IP (cont'd.)
Automatic Private IP Addressing (APIPA) address
  Addresses on the 169.254.0.0/16 network
  Designed as a solution for very small networks with no Internet connectivity requirements
Windows 7 also allows you to configure a static set of alternate IP configuration options
  If a DHCP server cannot be contacted, the alternate IP configuration is used instead

## Slide 24: Methods for Configuring IP (cont'd.)

## Slide 25: Essential IPv4 Utilities
Hostname command
  Displays host name of the computer that it is run on
ipconfig command
  Displays the basic TCP/IP settings of all active network connections
ping command
  Confirms basic IP connectivity between the computer that it is run on and a specified target host
tracert command
  Details an IP path through routers to a destination IP address

## Slide 26: Essential IPv4 Utilities (cont’d.)
pathping command
  Combines the functionality of the ping and tracert commands
route command
  Alters or display the IP routing table
netstat command
  Displays different types of TCP/IP statistics for active software and connections
nbtstat command
  Displays information about a connection using NBT

## Slide 27: Essential IPv4 Utilities (cont’d.)
getmac command
  Identifies the MAC address assigned to each adapter in the system
arp command
  Identifies the MAC addresses of computers that can directly communicate with the computer
netsh command
  Powerful script tool that can view or modify the computer’s network configuration
nslookup command
  Used at the command prompt to lookup a DNS entry

## Slide 28: Troubleshooting IPv4
Confirm current settings
  ipconfig and netsh utilities can display the current settings
Validate IPv4 connectivity
  ping utility can be used to confirm that the computer can ping its own loopback address
Verify DNS name resolution
  Confirm the correct DNS servers are specified on network settings
Verify data connections
  Problem may be a result of data filtering by a firewall

## Slide 29: IP version 6
Improvements found in IPv6 include:
  Increased address space
  Hierarchical routing to reduce the load on Internet backbone routers
  Simpler configuration through automatic address management
  Inclusion of encryption services for data security
  Quality of service
  Extensibility to support new features

## Slide 30: IPv6 Address Notation
Address space for IPv4 is nearing depletion
  IPv6 has a significantly larger address space
IPv6 addresses are 128 bits long
IPv6 has many more addresses than would normally be required for computing devices
IPv6 addresses are represented in hexadecimal, with each four-digit segment separated by colons
  Any group of four hex digits can drop leading zeros
  Long set of zeros can be compressed to a double colon

## Slide 31: IPv6 Address Types
Link-local Unicast
  Allows computers in a local network to communicate with each other without requiring the use of a router
Global Unicast
  Can be routed as a public address on the Internet through routers and networks
Unique Local Unicast
  Replacement address type for the deprecated site-local address type

## Slide 32: IPv6 Address Types (cont’d.)
Multicast
  Serves the same purpose as an IPv4 multicast address
Anycast
  Multiple devices can share the same anycast address and respond to other computers without an IP address conflict
Special addresses
  Two special addresses exist in IPv6, the loopback address and the unspecified address

## Slide 33: IPv6 Address Types (cont’d.)
Teredo
  Allows IPv6 data to be tunneled over an IPv4 network that is using Network Address Translation (NAT).

## Slide 34: Methods for Configuring IPv6
Windows 7 automatically configures its network interfaces with a link-local address
To configure IPv6, you can use:
  Static configuration
  Automatic configuration
  Scripts

## Slide 35: Troubleshooting IPv6 Settings
Confirm current settings
  Settings should be confirmed due to the default nature of IPv6 clients attempting to auto-configure themselves
Validate IPv6 connectivity
  ping utility can be used to confirm that the computer can ping its own loopback address
Verify DNS name resolution
Verify data connections
  Using the telnet application is a common tool for administrators to test application connectivity

## Slide 36: File Sharing
File sharing in Windows 7
  Allows you to share files from any folder on your computer or the Public folder
    With other computer users on your LAN

## Slide 37: Sharing the Public Folder
Sharing the Public folder
  Simplified way to perform file sharing
Files in the Public folder are shared between users who log on the local computer
  Can also be shared with network users
Options for sharing the Public folder
  Turn on sharing so anyone with network access can read and write files in the Public folder
  Turn off Public folder sharing

## Slide 38: Sharing the Public Folder (cont'd.)

## Slide 39: Sharing the Public Folder (cont'd.)
Options for Password protected sharing related to the Public folder
  Turn on password protected sharing
  Turn off password protected sharing

## Slide 40: Sharing Any Folder
Sharing files from any folder on your computer
  Gives you more options to control
    Which users have access to your files
    What those users can do to your files
You can set the permissions for users when you share individual folders
  Ability to configure permissions may be confusing for inexperienced users
In a domain-based network
  Can select users from the domain to share files with

## Slide 41: Sharing Any Folder (cont'd.)
In a workgroup-based network
  You must create local accounts for the users you want to share files with

## Slide 42: Creating and Managing Shared Folders
“Share with” menu option
  Simplifies folder sharing by controlling both NTFS permissions and share permissions at the same time
  Choices in the Share with menu
    Nobody
    Homegroup (Read)
    Homegroup (Read/Write)
    Specific people

## Slide 43: Creating and Managing Shared Folders (cont'd.)

## Slide 44: Creating and Managing Shared Folders (cont'd.)

## Slide 45: Creating and Managing Shared Folders (cont'd.)
Advanced Sharing
  Allows you to configure options that are not available in the simpler “Share with” interface
  Only configures share permissions
  When shared folder permissions are combined with NTFS permissions
    Most restrictive permissions are effective
  To simplify the management of permissions
    Assign Full Control share permission to the Everyone group
    Use NTFS permissions to control access to the files

## Slide 46: Creating and Managing Shared Folders (cont'd.)

## Slide 47: Creating and Managing Shared Folders (cont'd.)

## Slide 48: Creating and Managing Shared Folders (cont'd.)
Advanced Sharing (cont'd.)
  Settings you can configure in Advanced Sharing
    Share this folder
    Share name
    Limit the number of simultaneous users to
    Comments
    Permissions
    Caching
  Share permissions available in Windows 7
    Full Control
    Change
    Read

## Slide 49: Monitoring Shared Folders
Computer Management
  Most comprehensive way to monitor shares
Shared Folders System Tool has three nodes for monitoring and managing shared folders
  Shares
  Sessions
  Open Files

## Slide 50: Monitoring Shared Folders (cont'd.)

## Slide 51: Internet Connectivity
Topics
  Single-Computer Internet Connectivity
  Shared Internet Connectivity
  Internet Connection Sharing

## Slide 52: Single-Computer Internet Connectivity
Cable
  Almost all cable companies offer high-speed Internet connectivity
  You will be supplied with a cable modem
  By default, Windows 7 networking is configured to use DHCP to obtain IP configuration information
Digital subscriber line (DSL)
  High-speed Internet connection over telephone lines
  You will be supplied with a DSL modem
  Usually use Point-to-Point Protocol over Ethernet (PPPoE) to secure connection

## Slide 53: Single-Computer Internet Connectivity (cont’d.)
Dial-Up
  Much slower way to access the Internet
  Suitable for simple tasks such as reading e-mail and text-oriented Web pages
Wireless WAN
  Fully supported by Windows 7
  Most broadband vendors refer to this feature as “tethering” the computer to the mobile device

## Slide 54: Shared Internet Connectivity
Multiple computers can share a single Internet connection
  Common for cable modem and DSL connections
Common mechanisms for sharing an IP address
  Router
  Internet Connection Sharing (ICS)
Router or computer performing ICS is assigned the IP address from the ISP
  Computers on the internal network are assigned private IP addresses

## Slide 55: Shared Internet Connectivity (cont'd.)

## Slide 56: Shared Internet Connectivity (cont'd.)
Hardware routers sold in retail stores
  Simple firewalls that perform network address translation (NAT)
NAT is the process that allows multiple computers to share a single IP address
  ICS also performs NAT

## Slide 57: Internet Connection Sharing
ICS allows a Windows 7 computer to act as an Internet router
  Called the host computer
Host computer must have an Internet connection (public interface)
  Plus one additional network connection (private interface)
Use the Sharing tab in the Properties of the public interface to enable ICS

## Slide 58: Internet Connection Sharing (cont'd.)

## Slide 59: Wireless Networking
Wireless network
  Transfers data without a physical connection
Windows 7 provides a strong foundation for wireless technology
Wireless access point (WAP)
  Base station that connects to the wired network
Most common configuration details for a WAP:
  Security Set Identifier (SSID)
  802.11 mode
  Security method

## Slide 60: Creating a Wireless Connection
Several methods:
  Manually connect to a wireless network
  Connect to a Network
  Copy profile from USB flash drive
  Command line
  Group policy

## Slide 61: Managing Wireless Connections

## Slide 62: Troubleshooting Wireless Connections
Other devices, such as microwaves and cordless telephones, can interfere with the signal
Some 802.11 standards are limited to what channels, in addition to specific frequencies, they can use to communicate
Windows 7 client can be configured to connect to a WAP automatically when it is in range
WAP devices in public places may be untrusted, even if they have a pass-phrase configured

## Slide 63: Windows Firewall
Windows 7 includes an improved version of Windows Firewall to protect your computer
Standard firewall
  Protects your computer by restricting which network packets are allowed to reach your computer
Host-based firewall
  Evaluates each packet as it arrives and determines whether that packet is allowed or denied
One way to improve security on computers is by reducing the attack surface

## Slide 64: Windows Firewall (cont'd.)
Windows Firewall features
  Inbound filtering
  Outbound filtering
  Firewall rules combined with IPsec rules
  Support for complex rules
  Support for logging

## Slide 65: Basic Firewall Configuration
Windows Firewall Control Panel window
  Windows 7 allows custom firewall settings for each type of network location: home, work, or public
When Windows Firewall is enabled
  Default configuration blocks all incoming packets except for specifically configured exceptions
There is an option to block all incoming connections

## Slide 66: Basic Firewall Configuration (cont'd.)

## Slide 67: Basic Firewall Configuration (cont'd.)

## Slide 68: Basic Firewall Configuration (cont'd.)

## Slide 69: Advanced Firewall Configuration
Allows you to configure more complex rules, outgoing filtering, and IPsec rules
Tools available to perform advanced firewall configuration
  Windows Firewall and Advanced Security snap-in
  Netsh
  Group Policy
Configure Firewall Properties
  Windows 7 stores the firewall properties based on location types

## Slide 70: Advanced Firewall Configuration (cont'd.)

## Slide 71: Advanced Firewall Configuration (cont'd.)
Configure Firewall Properties (cont'd.)
  Configuration of each location type is called a profile
  Windows Firewall with Advanced Security on Local Computer node
    Shows the configuration of each profile
  In each profile, you can:
    Enable or disable Windows Firewall
    Configure inbound connections
    Configure outbound connections
    Customize settings
    Customize logging

## Slide 72: Advanced Firewall Configuration (cont'd.)
Configure Firewall Properties (cont'd.)
  IPsec is a system for securing and authenticating IP-based network connections
  IPsec settings you can configure
    Key exchange
    Data protection
    Authentication Method
  A large number of inbound and outbound rules are created by default in Windows 7

## Slide 73: Advanced Firewall Configuration (cont'd.)
You modify an existing rule by opening its properties
Tabs in the properties of an outbound rule
  General
  Programs and Services
  Computers
  Protocols and Ports
  Scope
  Advanced

## Slide 74: Advanced Firewall Configuration (cont'd.)
Create New Firewall Rules
  A wizard guides you through the process
Rule types you can create with the Outbound Rule Wizard
  Program
  Port
  Predefined
  Custom
Actions for a rule
  Allow the connection
  Allow the connection if it is secure
  Block the connection

## Slide 75: Advanced Firewall Configuration (cont'd.)
Create New Computer-Connection Security Rules
  Use IPsec to authenticate and secure communication between two computers
  Security rule types
    Isolation
    Authentication exemption
    Server-to-server
    Tunnel
    Custom

## Slide 76: Advanced Firewall Configuration (cont'd.)
Monitor Windows Firewall Rules and Connections
  Firewall node under Monitoring in the Windows Firewall with Advanced Security snap-in
    Allows you to see rules that are enabled in one screen
  Connection Security node under Monitoring
    Allows you to see the computer connection security rules that are enabled
      And any security associations that are active
  Security association
    Rules for communication between two computers

## Slide 77: Network Bridging
Network bridge in Windows 7
  Allows you to connect two separate networks, with Windows 7 acting as a bridge between them
Networks can be of different types
Computer acting as a network bridge must have two network cards to connect to each network
Technology is seldom used

## Slide 78: Ad hoc and Homegroup Networks
Networking for a small group of computers outside the corporate office is more about convenience
Two networking technologies that assist with that goal
  Ad hoc networking
  Homegroups

## Slide 79: Ad hoc Networking
Ad hoc network in Windows 7
  Allows you to configure an existing wireless network adapter on your computer as a rudimentary wireless access point (WAP)
Options and features are limited in comparison to a commercial WAP

## Slide 80: Homegroup Networks
Primarily uses IPv6 and link-local addresses to enable communications between homegroup members
Discovery of computers and their names on the local network is automatic by default
Computer can only create a homegroup when it has a network interface connected as a home network location and it is not domain joined
Security in a homegroup is simple
Windows automatically manages homegroup connections

## Slide 81: Summary
Network Sharing Center is a central location to view and access networking information
Windows 7 is network-aware and can sense which network location it is connected to
Network connections are composed of clients, services, protocols, and drivers
Windows 7 network architecture includes Winsock, TDI, and WSK interfaces
Important configuration concepts in IPv4 are IP addresses, subnet masks, default gateways, DNS, and WINS

## Slide 82: Summary (cont'd.)
Windows 7 can obtain IP configuration information from static configuration data, DHCP, APIPA, or an alternate IP configuration
Windows 7 uses IPv6 to support peer-to-peer networking applications
Sharing the Public folder is an easy way to share files on the network
When you share any folder you can use “Share with” or advanced sharing

## Slide 83: Summary (cont'd.)
The primary technologies for connecting to the Internet are cable, DSL, and dial-up
With ICS, there must be a mechanism to share the single IP address assigned by your ISP
Windows Firewall is a host-based firewall included with Windows 7
Network Bridging lets you connect two different network types as a single network
Ad hoc networks allow a Windows 7 computer to configure its wireless network adapter as a basic wireless access point